| Release Date | 2023.10.20 |
| --- | --- |
| TH4 V2（PSDK）firmware version | V01.01.01.46 |
| Supported Products and Firmware Version | DJI Skyport V2：V01.03.05.00 czi Assistant App：V1.0.6 |
|  | Matrice 300 RTK + DJI Smart ControllerEnterprise Matrice 300 RTK：V07.00.01.00 DJI Smart ControllerEnterprise：V07.00.01.01 DJI Pilot 2 App：V7.0.2.5 |
|  | Matrice 300 RTK + DJI RC Plus Matrice 300 RTK：V57.01.00.01 DJI RC Plus：V02.02.04.05 DJI Pilot 2 App：V7.1.0.32 |
|  | Matrice 350 RTK + DJI RC Plus Matrice 350 RTK：V07.01.00.01 DJI RC Plus：V02.02.04.05 DJI Pilot 2 App：V7.1.0.32 |

# Update content

- TH4 V2 PSDK version updated to 3.6.0_1883.

- Added long press recovery function. When the load mechanism gets stuck, a floating window message will display, and long pressing the load button will restore normal hook position.

# Note

- Make sure to upgrade czi Assistant, TH4 V2, aircraft, remote controller, DJI Skyport V2 firmware, and DJI Pilot 2 App to the latest versions, otherwise it will affect the usage.

- After the upgrade is completed, please remove the TF card and restart the catapult.

- When TH4 V2 is running on M350 aircraft, it only supports PILOT2 control.

# List of Known Issues

| Influenced Product | Problem Description | Avoidance Measures (Pick one of the measures, then the problem can be avoided) |
| --- | --- | --- |
| TH4 V2 GL60Plus czi Assistant | Using the DJI Matrice 300 RTK (DJI Smart ControllerEnterprise),the H20T, GL60Plus, and TH4 V2 can be mounted simultaneously. However, when the GL60Plus is mounted on the upper gimbal, the czi Assistant fails to recognize both the GL60Plus and TH4 V2. | Control using DJI Pilot 2 GL60Plus with under-mounted gimbal bracket |
| DJI H20T GL60Plus | When H20T, GL60Plus, and TH4 V2 are powered on simultaneously, H20T and GL60Plus fail to sync and follow. | First, synchronize the H20T and GL60Plus to enable follow mode, and then connect the TH4 V2. |

| Release Date | 2023.07.05 |
| --- | --- |
| TH4 V2（PSDK）firmware version | V01.01.01.45 |

# Update content

- Compatible with DJI Matrice 350 RTK drone.

# Upgrade method

Upgrade method 1:

TF card upgrade

1. Prepare a 4-32GB TF memory card and a card reader. The TF card format must be FAT32. Insert the TF card into the card reader, and then insert the card reader into the computer's USB port;

2. Put the compressed package in the root directory of the TF card;

3. Then unzip it directly to the current folder;

4. Mainly put the folder "PSDK_TH4_BL" in the root directory of the TF card. This folder contains the firmware to be upgraded;

5. Eject the TF card, remove the card reader, and take out the TF card;

6. Insert the TF card into the TF card slot next to the TH4 adapter ring;

7. Hang the TH4 on the drone and turn on the drone;

8. When the program upgrade is completed, the TH4 will automatically start;

9. Remove the TF card to complete the upgrade.

Save method

TF Format

Upgrade method 2:

Use DJI Smart ControllerEnterprise with czi Assistant online upgrade.

1.Use the DJI Smart ControllerEnterprise with an internet connection and open the czi Assistant app.

2.The czi Assistant app will recognize the TH4 payload. Click on "Check" and follow the prompts to upgrade. Download and upload the new firmware.

3.Once the firmware has been uploaded, the system will automatically restart the device. czi Assistant/DJI Pilot 2 APP will then recognize the payload and display the new firmware version, indicating that the upgrade is complete.

Upgrade Note:

1.The DJI Smart ControllerEnterprise must be connected to the internet for czi Assistant app online upgrades.

2.When performing an online upgrade, remove the TF card.

3.Only the M300 RTK with DJI Smart ControllerEnterprise supports czi Assistant online upgrades.